## Slide 1
End-to-End Intelligent Vision System for Automated Product Assembly, Defect Detection, and Segregation
Sridarshan A · Adhavan M · Sivapiriyan A R · Hariharasudhan D
Vishwakarma Application ID: VK26-IITI-AHM-0093
Notes: Introduce Team Cipher Core from Sri Ramakrishna Engineering College and the project in one sentence: a low-cost PLC + Raspberry Pi vision cell that assembles, inspects and sorts tap-cap assemblies.

## Slide 2
Project Overview
TEAM CIPHER CORE | SREC
2 / 18
5 Stations
INLINE PROCESS STAGES
4 Cylinders
PNEUMATIC ACTUATORS
24 V DC
PLC-CONTROLLED CELL
4 Checks
AUTOMATED VISION TESTS
Figure: 3D CAD view of the Cipher Core cell
Project Overview
Title: End-to-End Intelligent Vision System for Automated Product Assembly, Defect Detection, and Segregation
Team: Sridarshan A, Adhavan M, Sivapiriyan A R, Hariharasudhan, D
Institute: Sri Ramakrishna Engineering College
Team ID: VK26-IITI-AHM-0093 Track: Industrial Automation & Machine Vision
Core innovation: A low-cost PLC + Raspberry Pi vision cell that presses, inspects and sorts parts on the fly no proprietary smart camera needed.
Notes: Open with the one-line innovation: affordable, open-source industrial automation for MSMEs. Point to the four numbers: five stations, four cylinders, 24 V PLC control, four automated vision checks.

## Slide 3
Problem Statement & Target Beneficiary
TEAM CIPHER CORE | SREC
3 / 18
Component 1: base cap
Component 2: "LEO" top cap
Target Beneficiary
Local neighbourhood manufacturing units, MSMEs and regional assembly workshops.
Problem Statement
Pain point: Local units rely on manual assembly, pressing and visual quality control.
Impact: Fatigue, uneven pressing force and subjective checks let text smudges, scratches and improper mating gaps pass.
Gap: Industrial smart cameras and PLC vision systems exist, but their cost and locked-in proprietary software put them out of reach for MSMEs.
Fatigue & inconsistent force
Hand pressing varies from part to part and operator to operator.
Subjective inspection
Eyes miss smudged letters, scratches and hairline gaps.
Cost & vendor lock-in
Proprietary vision systems are unaffordable for small workshops.
Notes: Explain the two parts being assembled (clear base cap + white LEO-labelled top). The problem is manual pressing and eyeball inspection, and the fact that industrial vision systems are out of reach for small units.

## Slide 4
User Journey: Before vs After
4 / 18
BEFORE: Manual workflow
AFTER: Cipher Core automated cell
1
Operator places cover and label by hand
Slow, tiring loading step
1
Feeders drop parts; cylinder presses
Consistent pneumatic mating force
2
Pressed by hand, then turned over
Inconsistent force and ergonomic strain
2
C-bend flips the assembly 180°
Zero-energy, hands-free reorientation
3
Manual inspection of text and seams
Fatigue misses smudges and hairline gaps
3
Pi vision inspects every part
Objective, high-speed text and scratch check
4
Operator sorts good and bad components
Creates a bottleneck and slows output
4
Diverter ejects defects on the fly
Conveyor never stops
AUTOMATE
Outcome: hands-free assembly, objective inspection and zero-downtime sorting – fewer defects escaping, less rework, less operator fatigue.
Notes: Walk row by row: each manual step on the left is replaced by an automated step on the right. The cell removes hand pressing, eyeball inspection and manual sorting.

## Slide 5
Quantified Efficiency: How We Will Benchmark
5 / 18
Parameter | Manual process (before) | Cipher Core cell (after) | How we validate
Pressing force | Varies by operator and fatigue | Regulated pneumatic cylinder, fixed stroke | Gap / seating consistency over a batch
Inspection | Subjective, fatigue-prone eyeballing | Image subtraction + edge detection on every part | Detection rate on seeded-defect samples
Sorting | Manual; interrupts the flow | On-the-fly diverter; conveyor keeps moving | Rejects diverted with no conveyor stop
Operator involvement | Continuous handling and checking | Load feeders, empty bins | Manual touchpoints per part
Inspection cost | Proprietary smart camera + licences | Raspberry Pi + open-source OpenCV | BOM cost vs a commercial vision unit
Metrics tracked in Phase 5 testing: cycle time per part, defect-detection rate, false-reject rate and manual touchpoints – compared against the manual baseline.
Notes: Be clear that these are the measurable improvements. Baselines and results will be logged during integrated cell testing in Month 4.

## Slide 6
System Architecture: Block Diagram
6 / 18
1 Base Feeding
2 Mating & Pressing
3 C-Bend 180° Flip
4 Pi Vision Inspection
5 Pneumatic Sorting
Mechanical Structure
T-slot aluminum frame
Two gravity feeders + optical sensors
Conveyor and passive C-bend
Adjustable camera arch
Actuation & Power
4 double-acting cylinders
5/2 solenoid valves on one manifold
Press and diverter cylinders
24 V DC supply, conveyor drives
Electronic Controllers
Delta PLC, 24 V DC I/O
Raspberry Pi 4 + Pi Camera (CSI)
Optocoupler isolation boards
DIN-rail control cabinet
Firmware & Logic
OpenCV: image subtraction + edges
Pi outputs OK / NOT OK on GPIO
Ladder: latching, timers, counters
NC fail-safe interlocks
SIGNAL PATH: FROM VISION RESULT TO PNEUMATIC ACTION
Pi Camera (CSI)
Raspberry Pi (OpenCV)
GPIO 3.3 V
Optocoupler
PLC input
Solenoid + diverter
Notes: Top row is the physical process. The four cards are the subsystems. The bottom chain shows how a vision decision becomes a pneumatic action.

## Slide 7
Target Specifications & Hardware Selection
TEAM CIPHER CORE | SREC
7 / 18
Parameter | Target Spec | Selected Hardware / Protocol
Process | 5-station inline cycle: feed, press, flip, inspect, sort | Two gravity feeders with optical stack sensors; linear conveyor; passive C-type bend
Actuation | 4 double-acting cylinders, 25 mm × 50 mm | 5/2-way solenoid valves on a central manifold; 10 bar supply
Control | 24 V DC logic with latched, fail-safe operation | Delta PLC, WPLSoft ladder program; NC stop and interlock contacts
Vision | 4 checks per part: LEO text, smudges, scratches, air gap | Raspberry Pi 4 + Pi Camera (CSI), white LED lighting, OpenCV
Interface | Safe 3.3 V to 24 V signal transfer | Optocoupler isolation boards between Pi GPIO and PLC inputs
Sorting | On-the-fly rejection, conveyor never stops | Electro-pneumatic diverter cylinder into a reject bin
Structure & wiring | Rigid, reconfigurable, serviceable | T-slot aluminium extrusion, DIN rails, PVC ducts (24 V and 3.3 V separated)
Architecture rationale: optocoupler isolation lets a low-cost 3.3 V Raspberry Pi trigger industrial 24 V PLC logic safely.
Notes: Each row ties a target to the exact hardware chosen. Stress that all parts are standard, off-the-shelf industrial items.

## Slide 8
CAD Design: 3D Renders
TEAM CIPHER CORE | SREC
8 / 18
Figure: Isometric view of the complete assembly line
Camera arch and bins
Top view: conveyor and feeders
Key Mechanical Features
Feeders: stacked magazines with gate release drop base and top parts one by one.
C-bend: passive 180° gravity flip exposes the labelled side.
Vision arch: adjustable bracket holds the Pi Camera and LED lighting.
Sorting: diverter cylinder pushes NOT-OK parts into the reject bin.
Notes: Show the isometric model first, then the camera-arch view and the top view. Call out the feeders, C-bend, vision arch and reject bin.

## Slide 9
2D Engineering Drawing & Mechanical Specs
9 / 18
Figure: CAD 2D Diagram of the proposed system
Materials & Mechanical Specs
Frame: T-slot aluminium extrusion – rigid, light, re-configurable without welding.
Fastening: T-nuts and corner brackets hold cylinders and sensors steady under repeated pressing.
C-bend: passive gravity track – no motor, no energy.
Camera mount: articulating brackets for focus and shadow control.
Structural check: loads are light (plastic caps, 25 mm cylinders); FEA of the press mount is planned in fabrication.
Notes: The A3 drawing gives the orthographic and isometric views. Right-hand panel explains material and mounting choices.

## Slide 10
Electro-Pneumatic Circuit
TEAM CIPHER CORE | SREC
10 / 18
Figure: PLC I/O wiring and four cylinder circuits modelled in Automation Studio
Circuit Notes
Inputs (24 V): start trigger, four cylinder-extended sensors, Vision_Pass and conveyor transfer sensor.
Outputs: four solenoid coils (Sol 1–4) and the conveyor drives.
Pneumatics: 4 double-acting cylinders on 5/2 valves, 10 bar supply.
Digital twin: logic validated virtually before the hardware build.
Notes: This is the digital twin: four cylinders with 5/2 valves, PLC inputs and outputs. The logic was validated virtually before building hardware.

## Slide 11
Itemized Bill of Materials
12 / 18
Component | Specification | Qty | Sourcing
PLC | Delta PLC, 24 V DC I/O, WPLSoft programmable | 1 | Local industrial supplier
Edge computer | Raspberry Pi 4 | 1 | Local / authorised reseller
Camera & lighting | Pi Camera Module (CSI) + white LED module on articulating bracket | 1 | Local / electronics market
Pneumatic cylinders | Double-acting, 25 mm × 50 mm (press, diverter, feeder gates) | 4 | Local pneumatics supplier
Valves & manifold | 5/2-way 24 V DC solenoid valves on a central manifold block | 4 | Local pneumatics supplier
Conveyor | Linear transport with two drive motors | 1 set | Local fabrication
Sensors & isolation | Optical sensors for feeders and trigger; optocoupler boards 3.3 V to 24 V | 1 set | Local industrial / electronics
Frame & cabinet | T-slot extrusion, T-nuts, DIN rails, relays, 24 V supply, PVC ducts | 1 lot | Local suppliers
Procurement: all items are standard, off-the-shelf parts sourced locally – no imported specialty components.
Notes: Everything is a standard industrial part. Quantities come from the Automation Studio model and the mechanical design.

## Slide 12
Maker Journey: Stage 1 to Stage 2
13 / 18
Engineering Progress
Stage 1: defined the 5-station cell, feeders, vision approach and segregation.
3D CAD: full assembly modelled – isometric, top, feeder and camera views.
2D drawing: A3 sheet issued 08-10-2026.
Digital twin: 4-cylinder circuit built and simulated in Automation Studio.
PLC: ladder program written in Delta WPLSoft.
Vision: OpenCV approach set – image subtraction + edge detection on Pi 4.
Design evidence
Pneumatic and PLC Connection Circuits
2D CAD drawing
Notes: Summarise what changed between stages: complete CAD, the digital twin, PLC logic and a defined vision approach. Mention the team and the repository link.

## Slide 13
Safety & Hazard Mitigation
14 / 18
Failure Mode | Potential Hazard | Embedded Fail-Safe / Mitigation
Fault while press is active | Crush hazard at the pneumatic press | Hardwired NC loops instantly drop the output coils, de-energising the press safely.
Vision false accept / reject | Defective part passes or good part scrapped | Adjustable LED lighting removes shadows; golden-reference subtraction; one OK / NOT OK result to the PLC.
3.3 V GPIO meets 24 V logic | Damaged Pi, noisy or false signals | Optocoupler isolation boards; 3.3 V data and 24 V power routed in separate ducts.
Cylinder jam or air loss | Part mis-pressed or mis-sorted | Cylinder-extended sensors (Cyl 1–4) confirm each stroke before the PLC advances.
Feeder empty or jammed | Starved line, empty press cycles | Optical sensors confirm parts on each stack before release.
Physical Fail-Safes
Emergency-stop and machine guarding
Sensor interlocks on every actuator stroke
Hardwired NC fail safe loops
Standards Considered
ISO 4414 – pneumatic fluid power safety
IEC 60204-1 – electrical equipment of machines
ISO 12100 – machinery risk assessment
Notes: Lead with the hardwired NC fail-safe: any fault drops the output coils and de-energises the press. The FMEA covers the five most likely failures.

## Slide 14
Roadmap: 4-Month Fabrication Plan
15 / 18
Completed in Stage 2: 3D CAD and 2D drawing · Automation Studio digital twin · PLC ladder logic
1
MONTH 1
Vision Pipeline
Set up Pi 4 and camera
OpenCV: LEO text, smudge, scratch, air-gap checks
Order frame, cylinders and valves
2
MONTH 2
Mechanical Build
Assemble T-slot frame
Install conveyor, feeders and C-bend
Mount adjustable camera arch
3
MONTH 3
Pneumatics & PLC
Mount cylinders; pipe 5/2 valves to manifold
Wire optocouplers and ducts
Load ladder logic; integrate Pi
4
MONTH 4
Integration & Test
End-to-end cycle validation
Tune cycle time and diverter timing
Benchmark detection and rejection
Stage 3 target: a fully working prototype of feed, press, flip, inspect and sort ready for a live functional demonstration.
Notes: Design work is already done. The four months cover vision, mechanical build, pneumatics and PLC, then integrated testing leading to the Stage 3 demo.

## Slide 15
Technical Challenges & Risks
16 / 18
1
Low-contrast defects on translucent parts
A clear base cap and white label make smudges, hairline air gaps and scratches hard to see. Reflections and shadows can cause false results.
2
3.3 V vision vs 24 V industrial logic
Raspberry Pi GPIO cannot drive PLC inputs directly. A wrong interface risks damaging the Pi or creating noisy, false triggers.
3
On-the-fly rejection timing
The diverter must fire exactly as a flagged part passes, with the conveyor still running and no dwell time to correct a late decision.
4
Passive flip and feeding consistency
The gravity C-bend must flip every part exactly 180° and the feeders must release one part at a time without jams or double feeds.
Notes: These are the four anticipated bottlenecks from the design stage; the next slide gives the matching mitigations.

## Slide 16
Potential Solutions & Risk Mitigation
17 / 18
Risk | Primary solution | Backup / fallback
Low-contrast defects | Adjustable white LED lighting and shadow control; golden reference image subtraction plus edge detection; thresholds tuned in Phase 1. | Switch to back-lighting or low-angle lighting; add a second inspection angle.
3.3 V / 24 V interface | Optocoupler isolation boards between Pi GPIO and PLC inputs; data and power in separate ducts. | Swap in a relay interface board.
Rejection timing | Sensor-triggered tracking with a PLC timer delay between inspection and diverter, tuned during cell testing. | Reduce conveyor speed or add a second trigger sensor.
Flip and feed consistency | Adjustable C-bend geometry and press fixtures; optical sensors confirm each stack before release. | Add guide rails or a small pneumatic assist at the bend.
Design principle: modular subsystems – lighting, interface and bend can each be changed without redesigning the whole cell.
Notes: Every risk has a primary fix and a backup. The modular design means any subsystem can be swapped without redesigning the cell.

## Slide 17
References & Sources
18 / 18
Reference | Used for | Source
OpenCV documentation | Image subtraction and edge-detection pipeline | docs.opencv.org
Raspberry Pi documentation | Raspberry Pi 4 and Camera Module (CSI) interfacing | raspberrypi.com/documentation
Delta PLC and WPLSoft | Ladder programming | deltaww.com
Automation Studio | Electro-pneumatic circuit simulation | Famic Technologies
ISO 4414 | Pneumatic fluid power safety rules | iso.org
IEC 60204-1 | Electrical equipment of machines | iec.ch
Image sources: All photographs, CAD renders, engineering drawings, circuit and ladder screenshots in this deck are original work of Team Cipher Core, Sri Ramakrishna Engineering College.
Notes: Tools, documentation and standards used. All images are the team’s own work.